## Slide 1
SWE4005- Storage Technology and Management
Direct Attached Storage and Introduction to SCSI

## Slide 2: Chapter Objective
Upon completion of this chapter, you will be able to:
Discuss the benefits and challenges of DAS
Discuss DAS management options
Discuss evolution of SCSI
Describe SCSI – 3 architecture
Discuss SCSI addressing and communication model

## Slide 3: Host Access to Data
Data is accessed and stored by applications using the underlying infrastructure.
The key components of this infrastructure are the operating system (or file system), connectivity, and storage.
The storage device can be internal and (or) external to the host.
Host controller card accesses the storage devices using predefined protocols, such as IDE/ATA, SCSI, or Fibre Channel (FC).
External storage devices can be connected to the host directly or through the storage network.
When the storage is connected directly to the host, it is referred as direct-attached storage (DAS)

## Slide 4: Data access
Data can be accessed over a network in one of the following ways:
  block level,
  file level, or object level.

## Slide 5: Direct Attached Storage
Upon completion of this lesson, you will be able to:
Discuss the benefits of DAS
Describe the elements of DAS
Discuss DAS management considerations
Discuss DAS challenges

## Slide 6: What is DAS?

## Slide 7: DAS Benefits
Ideal for local data provisioning
Quick deployment for small environments
Simple to deploy
Low capital expense
Low complexity

## Slide 8: DAS Connectivity Options
ATA (IDE) and SATA
  Primarily for internal bus
SCSI
  Parallel (primarily for internal bus)
  Serial (external bus)
FC
  High speed network technology

## Slide 9: DAS Management
Internal
  Host provides:
    Disk partitioning (Volume management)
    File system layout
  Direct Attached Storage managed individually through the server and the OS
External
  Array based management
  Lower TCO (Total Cost of Ownership) for managing data and storage Infrastructure

## Slide 10: DAS Challenges
Scalability is limited
  Number of connectivity ports to hosts
  Difficulty to add more capacity
  Limited bandwidth
  Distance limitations
Downtime required for maintenance with internal DAS
Limited ability to share resources
  Array front-end port
  Unused resources cannot be easily re-allocated
  Resulting in islands of over and under utilized storage pools

## Slide 11: Introduction to SCSI
Upon completion of this module, you will be able to:
Describe SCSI-3 architecture
Discuss SCSI device models with different port configurations
Describe SCSI Addressing
Notes: https://www.youtube.com/watch?v=A3q1x3_7tTg

## Slide 12: Evolution of Parallel SCSI
Developed by Shugart Associates & named as SASI (Shugart Associates System Interface)
ANSI acknowledged SCSI as an industry standard
SCSI versions
  SCSI–1
    Defined cable length, signaling characteristics, commands & transfer modes
    Used 8-bit narrow bus with maximum data transfer rate of 5 MB/s
  SCSI–2
    Defined Common Command Set (CCS) to address non-standard implementation of the original SCSI
    Improved performance, reliability, and added additional features
  SCSI–3
    Latest version of SCSI

## Slide 13: SCCI Architecture
SCSI command protocol
  Primary commands common to all devices
Transport layer protocol
  Standard rules for device communication and information sharing
Physical layer interconnect
  Interface details such as electrical signaling methods and data transfer modes

## Slide 14: SCSI Device Model

## Slide 15
Device requests uses Command Descriptor Block (CDB)
  8 bit structure
  Contain operation code, command specific parameter and control parameter
SCSI Ports
  SCSI device may contain initiator port, target port, target/initiator port
  Based on the port combination, a SCSI device can be classified as an initiator model, a target model, a target model with multiple ports or a combined model (target/initiator model). Example:
    Target/initiator device contain target/initiator port and can switch orientations depending on the role it plays while participating in an I/O operation
  To cater to service requests from multiple devices, a SCSI device may also have multiple ports (e.g. target model with multiple ports)

## Slide 16: SCSI ADDRESSING
Notes: Ctd- controller/ target/device

## Slide 17: Example