## Slide 1
SWE4005- Storage Technology and Management
Storage Networking Technologies
Click to add text
Click to add text
Click to add text

## Slide 2: Modules

## Slide 3: Network-attached storage (NAS)
Upon completion of this module, you should be able to:
  Describe NAS, its benefits, and components
  Discuss NAS file-sharing protocols
  Describe different NAS implementations
  Describe file-level virtualization

## Slide 4: NAS Components and Benefits
During this lesson the following topics are covered:
  File sharing technology evolution
  Benefits of NAS
  NAS components
  NAS file sharing protocols
  NAS I/O operations

## Slide 5: File Sharing Environment
File sharing enables users to share files with other users
Creator or owner of a file determines the type of access to be given to other users
File sharing environment ensures data integrity when multiple users access a shared file at the same time
Examples of file sharing methods:
  File Transfer Protocol (FTP)
  Distributed File System (DFS)
  Network File System (NFS) and Common Internet File System (CIFS)
  Peer-to-Peer (P2P)

## Slide 6: File Sharing Technology Evolution

## Slide 7: What is NAS?
It is an IP-based, dedicated, high-performance file sharing and storage device.
NAS
Enables NAS clients to share files over IP network
Uses specialized operating system that is optimized for file I/O
Enables both UNIX and Windows users to share data
Notes: NAS - file level access to storage,
The management of file system is with remote storage.
NAS – uses existing data infrastructure.

## Slide 8: General Purpose Servers Vs. NAS Devices

## Slide 9: Benefits of NAS
Improved efficiency
Improved flexibility
Centralized storage
Simplified management
Scalability
High availability – through native clustering and replication
Security – authentication, authorization, and file locking in conjunction with industry-standard security
Low cost
Ease of deployment

## Slide 10: Components of NAS

## Slide 11: NAS File Sharing Protocols
Two common NAS file sharing protocols are:
  Common Internet File System (CIFS)
  Network File System (NFS)

## Slide 12: Common Internet File System
Client-server application protocol
  An open variation of the Server Message Block (SMB) protocol
Enables clients to access files that are on a server over TCP/IP
Stateful Protocol
  Maintains connection information regarding every connected client
  Can automatically restore connections and reopen files that were open prior to interruption

## Slide 13: Network File System
Client-server application protocol
Enables clients to access files that are on a server
Uses Remote Procedure Call (RPC) mechanism to provide access to remote file system
Currently, three versions of NFS are in use:
  NFS v2 is stateless and uses UDP as transport layer protocol
  NFS v3 is stateless and uses UDP or optionally TCP as transport layer protocol
  NFS v4 is stateful and uses TCP as transport layer protocol

## Slide 14: NAS I/O Operation

## Slide 15
The requestor packages an I/O request into TCP/IP and forwards it through the network stack. The NAS device receives this request from the network.
The NAS device converts the I/O request into an appropriate physical storage request, which is a block-level I/O, and then performs the operation against the physical storage pool.
When the data is returned from the physical storage pool, the NAS device processes and repackages the data into an appropriate file protocol response.
The NAS device packages this response into TCP/IP again and forwards it to the client through the network.

## Slide 16: NAS Implementation
Unified NAS
Has all of its components and storage system in a single enclosure or frame
Gateway NAS
NAS head shares its storage with SAN environment.
Scale-out NAS
Ideal for enterprise data centers
Consolidating both virtualized and non-virtualized file storage into one storage pool with a single point of management

## Slide 17: NAS Implementation – Unified NAS
Consolidates NAS-based (file-level) and SAN-based (block-level) access on a single storage platform
Supports both CIFS and NFS protocols for file access and iSCSI and FC protocols for block level access
Provides unified management for both NAS head and storage
FC Port
iSCSI Port
Ethernet
Port
Unified NAS
Block Data Access
File Access
Block Data Access
Ethernet
iSCSI SAN
FC SAN
iSCSI Hosts
FC Hosts
NAS Clients

## Slide 18: NAS Implementation – Unified NAS Connectivity
NAS head has front-end Ethernet ports which connect to IP.
  Front-end ports: provide connectivity to clients
  Back-end ports: provide connectivity to storage controllers
iSCSI and FC ports on a storage controller
  Enable hosts to access the storage directly or through a storage network at the block level.
FC Port
iSCSI Port
Ethernet
Port
Unified NAS
Block Data Access
File Access
Block Data Access
Ethernet
iSCSI SAN
FC SAN
iSCSI Hosts
FC Hosts
NAS Clients

## Slide 19: NAS Implementation – Gateway NAS
Uses external and independently-managed storage
  NAS heads access SAN-attached or direct-attached storage arrays
NAS heads share storage with other application servers that perform block I/O
Requires separate management of NAS head and storage
The gateway NAS is the most scalable because NAS heads and storage arrays can be independently scaled up when required.
Gateway NAS enables high utilization of storage capacity by sharing it with SAN environment.

## Slide 20: NAS Implementation – Gateway NAS
Application Servers
Gateway NAS
Storage Array
Application Server
Client
Client
Client
IP
FC SAN

## Slide 21: Gateway NAS Connectivity
Application Servers
Gateway NAS
Storage Array
Application Server
Client
Client
Client
IP
FC SAN
Communication between the NAS gateway and the storage system in a gateway solution is achieved through a traditional FC SAN.

## Slide 22: NAS Implementation – Scale-out NAS
Pools multiple nodes together in a cluster that works as a single NAS device
  Pool is managed centrally
Scales performance and/or capacity with addition of nodes to the pool non-disruptively
Creates a single file system that runs on all nodes in the cluster
  Clients, connected to any node, can access entire file system
  File system grows dynamically as nodes are added
Stripes data across all nodes in a pool along with mirror or parity protection

## Slide 23
InfiniBand Switches
Internal Switch 2
Internal Switch 1
Node 1
External Switch
Node 2
Node 3
InfiniBand is a networking technology that provides a low-latency, high-bandwidth communication link between hosts and peripherals.

## Slide 24: NAS Use Case 1 – Server Consolidation with NAS
UNIX
File Server
UNIX Client
Windows Client
Windows File Server
UNIX Client
Windows Client
NAS Device
Traditional File Server Environment
NAS Environment
IP
IP

## Slide 25: NAS Use Case 2 – Storage Consolidation with NAS
Web and Database
Servers
Windows File Server
UNIX
File Server
Business Clients
Storage
Internal Users
Surfers, Shoppers
Web and Database
Servers
NAS
Head
Business Clients
Storage
Internal Users
Surfers, Shoppers
Traditional File Server Environment
NAS Environment
IP
IP
FC SAN
FC SAN

## Slide 26: File-level Virtualization
Eliminates dependency between data accessed at the file-level and the location where the files are physically stored
Enables users to use a logical path, rather than a physical path, to access files
Uses global namespace that maps logical path of file resources to their physical path
Provides non-disruptive file mobility across file servers or NAS devices

## Slide 27
File Sharing Environment
Before File-level Virtualization
Storage Array
NAS Head
Clients
Clients
After File-level Virtualization
Clients
Clients
Storage Array
Virtualization
Appliance
NAS Head
NAS Head
NAS Head
File Sharing Environment
Dependency between client access and file location
Underutilized storage resources
Downtime is caused by data migrations
Break dependencies between client access and file location
Storage utilization is optimized
Non-disruptive migrations

## Slide 28: Concepts in Practice
EMC Isilon
EMC VNX Gateway

## Slide 29: EMC Isilon
Scale-out NAS solution
Includes ‘OneFS’ operating system that creates a single file system across Isilon cluster
Provides ability to nondisruptively add nodes to Isilon cluster
Includes ‘SmartPools’ that enables different node types to be mixed in a single cluster
Monitors component health and transparently reallocates files
Uses ‘Autobalance’ that rebalances data automatically, when a new node is added to the cluster
Uses ‘FlexProtect’ that protects from up to four simultaneous failures of either nodes or individual drives

## Slide 30: EMC VNX Gateway
Gateway NAS solution
Provides multi-protocol network file system access, dynamic expansion of file systems, high availability, and high performance
Comprises one or more NAS heads, called ‘X-Blades’ that run VNX operating environment
Includes ‘Control Station’ that provides a single point for configuring X-Blades